## Slide 1
Lab 1
Basic Network Setup
& Connectivity
CSIT491 - Network and Cybersecurity Lab
Anthony Castellanos • Imran Ahmed • Murtaza Syed
Nicolas Hoyos • Shaied Uddin

## Slide 2
Lab Objectives
1
Identify and label each device in the network diagram
2
Assign a static IP address to PC0 and configure DHCP on the router for PC1 and PC2
3
Use the ping command to verify connectivity between all devices
4
Use ipconfig to confirm network settings on each PC

## Slide 3
Equipment & Tools
Router
1x Cisco 2911 (GigabitEthernet Interface)
Switch
1x Cisco 2960-24TT (24-port)
End Devices
3x PCs — 1 static IP, 2 DHCP
Software
Cisco Packet Tracer
Network: 192.168.1.0 / 24 Gateway: 192.168.1.1 PC0: 192.168.1.50 (Static) PC1: 192.168.1.11 (DHCP) PC2: 192.168.1.12 (DHCP)

## Slide 4
Network Topology
[ Insert Screenshot ]
Packet Tracer Network Topology Screenshot
Router0 (Gi0/0): 192.168.1.1 | PC0: 192.168.1.50 (Static) — Fa0/2 | PC1: 192.168.1.11 (DHCP) — Fa0/3 | PC2: 192.168.1.12 (DHCP) — Fa0/4

## Slide 5
Router Configuration
Interface Setup
interface GigabitEthernet0/0
ip address 192.168.1.1
255.255.255.0
no shutdown
exit
Verify
do show ip interface brief
Gi0/0 192.168.1.1
YES manual up up
[ Insert Screenshot ]
show ip interface brief — Gi0/0 up/up

## Slide 6
DHCP Configuration
DHCP Pool — LAN_POOL
Exclude static addresses
ip dhcp excluded-address
192.168.1.1 192.168.1.10
Create pool
ip dhcp pool LAN_POOL
network 192.168.1.0
255.255.255.0
default-router 192.168.1.1
dns-server 8.8.8.8
exit
write memory
DHCP Pool Summary
Pool Name
LAN_POOL
Network
192.168.1.0 / 255.255.255.0
Excluded
192.168.1.1 – 192.168.1.10
Assignable Range
192.168.1.11 – 192.168.1.254
Default Gateway
192.168.1.1
DNS Server
8.8.8.8

## Slide 7
PC IP Configuration
PC0 — Static IP (192.168.1.50)
PC1 — DHCP (192.168.1.11)
PC2 — DHCP (192.168.1.12)
[ Insert Screenshot ]
PC0 — ipconfig
[ Insert Screenshot ]
PC1 — ipconfig
[ Insert Screenshot ]
PC2 — ipconfig

## Slide 8
Ping Testing
✓ All Pings Successful
All Pings Successful
PC0 → Router0
ping 192.168.1.1
Success
PC0 → PC1
ping 192.168.1.11
Success
PC0 → PC2
ping 192.168.1.12
Success
[ Insert Screenshot ]
PC0 Command Prompt — Ping Results

## Slide 9
Ping Verification — PC1
✓ Bidirectional Communication Confirmed
Bidirectional Communication Confirmed
PC1 — Ping to PC0 (192.168.1.50)
[ Insert Screenshot ]

## Slide 10
Complete Testing Summary
All Tests Successful
PC0 → Router0
Gateway
✓ Success
PC0 → PC1
Cross-device
✓ Success
PC0 → PC2
Cross-device
✓ Success
PC1 → PC0 (Static)
Bidirectional
✓ Success

## Slide 11
Lab 1 Successfully Completed
✓ Static and DHCP addressing configured successfully
✓ DHCP pool verified — addresses assigned to PC1 and PC2
✓ All ping tests passed — 4/4 replies, 0% packet loss
✓ All lab objectives achieved